## Slide 1
Gauthier Plagne
accurate SOC measurement for HEV and EV battery packs application

## Slide 2: CAB300 Features
CAB 300-C
Waterproof
sumitomo connector
Features:
  Fluxgate technology
  Current range up to +/- 350A
  Offset error lower than 10mA
  Linearity error < 0.1%
  Global error < 1% (over temperature)
  Ambient temperature: -40°C… +105°C
  Digital output (CAN)
  Vehicle 12V battery supply
  Sensor can provide either instantaneous or average value
  Bandwidth < 500Hz
  2 connector type available
CAB 300-C SP1
Tyco connector
Near-zero offset and accuracy on full current range gives strong advantage on hybrid market

## Slide 3: Current transducer comparison table
Parameter | CAB300-C SP2 | DHAB S/18 | HAH1BV S/24
Offset error | +/-10 mA | +/- 0.3A | +/-1.5 A
Global error at 30A (XG) | 50 mA | +/- 1.05 A | +/-2.1 A
Global error at 300A (XG) | 1500 mA | +/- 15 A | 8 A
Output type | CAN | Voltage, dual range | Voltage
Relative price (compared with HAH1) | 4 | 2 | 1
All accuracy data are give under -40/+85°C temperature range
At high current, error is mainly due to gain and linearity errors
At low current, error is mainly due to offset error

## Slide 4: Transducer error on SOC measurement
Target: Need to know the state of charge (SOC) of the battery taking into account the charge and discharge phase
Over a cycle, charge and discharge areas are equal
Discharge
Charge
Time
I(A)
A CT gain error will add a constant factor than multiplies the measurement
Over one cycle the areas measured will be equal (error is the same on positive or negative values)
An CT offset error will add a constant value to the measurement
This can lead to error on SOC measurement because charge and discharge areas will not be equals
SOC error
SOC error

## Slide 5: SOC error – Example on one current profile
  Reference sensor: - 513mA.h
  DHAB 2 ranges: -528mA.h (2.86%)
  CAB300: -514mA.h (0.1%)
SOC error: The bill
Battery pack price: 7000USD
Over-size of the battery to compensate SOC error:
7000x2.86% = 200 USD
Could worth to pay a little extra on the current transducer…